## Slide 1
Mobile Network Diagnostics

## Slide 2
Introduction
Mobile Data
Signal Issues
Roaming Issues

## Slide 3: Introduction
The purpose of this pack is to provide our clients with a Knowledge Guide to help with common network issue diagnostics.
By following the steps here, partners and customers can confidently complete some of the basic troubleshooting steps that the different Networks ask of Zest4 as part of their first line diagnostic checks. This will help drive customer satisfaction, making sure things are done right first time.

## Slide 4: Mobile Data
Mobile data
This diagnostic guide is designed for customers who have no data connectivity / poor or intermittent connectivity.
Second slide in this section is a “How to” page for settings - this is dependant on the device software being on the most up-to-date version, so please check this with the device user.
Apple and Android

## Slide 5
Toggle Mobile data Off and On.
Does this resolve the
Issue?*
Have any Alert Notifications been sent to
suggest that the number has been barred /
data allowance reached??
Switch the device off
and back on. Did
that work?
No
Ensure Device Network
Mode is set to Automatic.*
Does this resolve
the problem (ask customer
to try logging into bbc.co.uk)?
Resolved
Yes
Resolved -
Check the portal to see if any
bars are present
and if more data is needed.
Yes
Resolved
Yes
Resolved
No
Time to call Zest4
Mobile Data
No
No
Yes
This path is for mobile data issues – data not working, slow or intermittent data connection. This path will work for both iPhone and Android devices.
* I have added on the next slide, a section to show you how to find the particular settings we are asking the user to check/amend. This is on the condition the device is on the most up-to-date software version – Always check to see all device updates have been completed.

## Slide 6
iPhone
From the Lock Screen, swipe up to access the Home Screen
Tap Settings
Tap Mobile Data
Tap the slider against Mobile Data
Android
From the Home Screen, swipe Up
Tap Settings
Tap Connections
Tap Data usage
Tap the slider against Mobile data
Tap OK
Android
From the Home Screen, swipe Up
Tap Settings
Tap Connections
Tap Mobile networks
Tap Network mode
Tap the required Network mode
iPhone
From the Lock Screen, swipe up to access the Home Screen
Tap Settings
Tap Mobile Data
Tap Mobile Data Options
Tap Voice & Data
Tap the required Network mode
Tap Back
Toggle Mobile Data Off and On again.
Does this resolve the
Issue?*
Ensure Network
Mode is set to: Automatic.
Does this resolve
the issue (ask customer
to try logging into bbc.co.uk)?
Mobile Data - How to Check Settings

## Slide 7: Signal Issues
This diagnostic is designed to support customer with no/poor signal /poor signal .
Apple and Android

## Slide 8
Check SIM number
with the user and ensure that it
matches what you can see
on the Zest4 portal.
Check mobile data is
Enabled on the device.
Is the issue affecting just
the one user, or multiple
users in the same location?
Before issue started, did the
user have good signal?
Ensure Device Network Mode
is set to: Automatic.
Manually Roam on to a
different network, and then
back to your Home network.
Turn device off and back
on – has this resolved
Issue?
Time to call
Zest4
These Diagnostic steps are for customers with no signal at all. Checking the SIM first, will eliminate any obvious issues. Again, always make sure the device software is up-to-date.
Also, it is a good idea to check the relevant Network Coverage Checker as well (see Slide 9 for links).
This diagnostic path works for both Apple and Android users.
Signal Issues – No Signal

## Slide 9: UK Network Coverage Checkers
https://www.o2.co.uk/coveragechecker
https://www.vodafone.co.uk/network/status-checker
https://coverage.ee.co.uk/coverage/ee

## Slide 10
How does the poor
signal affect you?
Outgoing calls
Incoming calls
Dropped calls
Data Issues
Is the issue affecting a single
user or multiple users?
Ensure Device Network Mode
Is set to Automatic.
Manually roam on to
another network, then
back to your Home network.
Turn device Off and back
On again – has this resolved
Issue?
Time to call
Zest4
These additional steps are for dropped calls only.
Is every call dropping?
Regardless of answer,
Please take call examples
Ask customer to collect 3
examples of dropped calls
over recent 72hrs. Include:
Date / Time / Postcode *
* Please note the examples to be given to Zest4 within that 72hr period. Anything outside of this timeframe will not be counted and would need to be collated again.
Are you connected to
Wi-Fi Calling when the
calls drop?
Signal Issues – Poor Signal

## Slide 11
Roaming
Roaming – Data issues
This Diagnostic is designed for customers with poor or no data connectivity while abroad
Roaming – unable to make voice calls
This Diagnostic is designed for customer who can’t make calls or struggle to call some numbers while abroad
Roaming Issues
Roaming – No Connectivity
This Diagnostic is designed to assist users who have no signal at all on when roaming abroad.
Roaming – Unable to make voice calls
This Diagnostic is designed for users who cannot make calls, or struggle to call some numbers while abroad.
Roaming – Data issues
This Diagnostic is designed for users with poor or no data connectivity while roaming abroad.

## Slide 12
Roaming Issues: No Connectivity (Apple)
General Housekeeping:
Has the customer turned
on data roaming?
Has the customer tried
to turn Aeroplane mode
on and off?
Is this issue affecting more
than just the customer
i.e. anyone else
they are with?
Is this happening in more
than one location?
Has the user had any
roaming issues before?
If none of the General
Housekeeping works. then
continue with
Diagnostics.
Perform a manual
Network search
From the Lock Screen, swipe up to access the Home Screen
Tap Settings
Tap Mobile Data
Tap Network Selection
Tap the slider against Automatic to turn off
Tap the Network to connect to
Tap Back
Manually logged on to a
Roaming network. Does
this resolve issue?
Please note this activity cannot be completed during a call on the device.
De-activate any Wi-Fi connection and then within the network settings of the device the customer is able to switch the device from an Automatic network selection to Manual.
By doing this the device will search and find any network operators that provide coverage in the area. This includes networks that the home networks don't have any roaming agreements with. To ensure the user is exploring all options, get the user to attempt to log on to ALL available networks that appear in the search and test before moving on to the next one.
IMPORTANT: If no networks show up in the list (only the one that the customer is already connected to) when carrying out the search, select No networks found. This is because you cannot log off the current network and log on to another.
Ensure Automatic mode is re-enabled after testing in Manual mode.
If the menu option is not available ensure that the SIM card is inserted correctly and securely locked in place. Referring to the device manual should show how to correctly insert the SIM.
No
Time to call
Zest4

## Slide 13
Ensure Mobile data
Switching is enabled. Does
this resolve the issue?
If the customer is using the Dual SIM functionality on the handset and wants to use mobile data whilst on a call, they will need to be using the same line which is set up for Mobile Data – unless they have Mobile Data Switching activated. Once Mobile Data Switching is enabled, any time the customer tries to establish a Mobile Data connection whilst on a call, it will automatically switch to the other line if needed – this does not change the default data line.
Apple Support - Using Dual SIM with an eSIM
Enable data roaming on
the device. Does this
resolve the problem?
From the Lock Screen, swipe up to access the Home Screen
Tap Settings
Tap Mobile Data
Tap Mobile Data Options
Tap the slider against Data Roaming PSSST... Check the user’s mobile number to make sure Roaming is enabled and offer any available Roaming bundles, if not included in their plan.
If none of the above steps have worked…..
Time to call
Zest4
Roaming Issues: Data (Apple)
General Housekeeping:
Has the customer turned
on data roaming?
Has the customer tried
to turn Aeroplane mode
on and off?
Is this issue affecting more
than just the customer
i.e. anyone else
they are with?
Is this happening in more
than one location?
Has the user had any
roaming issues before?
If none of the General
Housekeeping works. then
continue with
Diagnostics.
Open Settings
2 Tap Mobile Data
Tap Mobile Data again at the top of the screen
Tap Mobile Data switching to enable (green) and disable (grey)
After each step have customer try to use data by googling something or looking up www.bbc.co.uk

## Slide 14
Is the device showing signal
strength? If no follow path
for No Signal.
The signal strength indicator is at the top of the screen.
If there's no signal displayed, the device will usually show a message such as No service or Emergency calls only.
If the customer has at least one bar or more displayed, it means that they're connected to the network and the device does have signal strength.
Some devices may show an 'R' next to the signal strength indicator which would mean that the customer is roaming.
Switch device off/on and
Retest. Does this resolve the
issue?
Perform a manual
Network search
From the Lock Screen, swipe up to access the Home Screen
Tap Settings
Tap Mobile Data
Tap Network Selection
Tap the slider against Automatic to turn off
Tap the Network to connect to
Tap Back
Manually logged on to a
Roaming network. Does
this resolve issue? ( test
call)
Please note this activity cannot be completed during a call on the device.
De-activate any Wi-Fi connection and then within the network settings of the device the customer is able to switch the device from an automatic network selection to a manual.
By doing this the device will search and find any network operators that provide coverage in the area. This includes networks that your home network might not have any roaming agreements with. To ensure the user is exploring all options, get the customer to attempt to log on to ALL available networks that appear in the search and test before moving on to the next one.
IMPORTANT: If no networks show up in the list (only the one that the customer is already connected to) when carrying out the search, select No networks found. This is because you cannot log off the current network and log on to another.
Ensure automatic mode is re-enabled after testing in manual mode.
If the menu option is not available ensure that the SIM card is inserted correctly and securely locked in place. Referring to the device manual should show how to correctly insert the SIM.
If the above diagnostics do not work, then please contact Zest4
Zest4
Roaming Issues: Unable to Make Voice Calls (Apple)
General Housekeeping:
Has the customer turned
on data roaming?
Has the customer tried
to turn Aeroplane mode
on and off?
Is this issue affecting more
than just the customer
i.e. anyone else
they are with?
Is this happening in more
than one location?
Has the user had any
roaming issues before?
If none of the General
Housekeeping works. then
continue with
Diagnostics.

## Slide 15
Roaming Issues: No Connectivity (Android)
General Housekeeping:
Has the customer turned
on data roaming?
Has the customer tried
to turn aeroplane mode
on and off?
Is this affecting more
than just the customer i.e
anyone they are with? *
Is this happening in more
than one area?
Have you had issues
roaming before?
If none of the General
Housekeeping works
continue with
Diagnostics.
Perform a manual
Network search
From the Home Screen, swipe Up
Tap Settings
Tap Connections
Tap Mobile networks
Tap Network operators
Tap the slider against Select automatically to turn off
Tap OK
Tap the Network to connect to
Manually logged on to a
Roaming network. Does
this resolve issue?
Same steps as above – ask customer to select first or second network on list
Please note this activity cannot be completed during a call on the device.
De-activate any Wi-Fi connection and then within the network settings of the device the customer is able to switch the device from an automatic network selection to a manual.
By doing this the device will search and find any network operators that provide coverage in the area. This includes networks that the home network don't have roaming agreements with. To ensure the customer is exploring all options, get the customer to attempt to log on to ALL available networks that appear in the search and test before moving on to the next one.
IMPORTANT: If no networks show up in the list (only the one that the customer is already connected to) when carrying out the search, select No networks found. This is because you cannot log off the current network and log on to another.
Ensure automatic mode is re-enabled after testing in manual mode.
If the menu option is not available ensure that the SIM card is inserted correctly and securely locked in place. Referring to the device manual should show how to correctly insert the SIM.
No
Time to call
Zest4

## Slide 16
Ensure Mobile data
Switching is enabled. Does
this resolve the issue?
From the Home Screen, swipe Up
Tap Settings
Tap Connections
Tap Mobile networks
Tap the slider against Data roaming PSSST... Check the customer's account to make sure Roaming is enabled and promote any available Roaming bundles if not included in their plan. Also advise to turn off Wi-Fi Calling when leaving the UK as this could incur extra charges
If none of the above steps have worked…..
Time to call
Zest4
Roaming Issues: Data (Android)
General Housekeeping:
Has the customer turned
on data roaming?
Has the customer tried
to turn aeroplane mode
on and off?
Is this affecting more
than just the customer i.e
anyone they are with? *
Is this happening in more
than one area?
Have you had issues
roaming before?
If none of the General
Housekeeping works
continue with
Diagnostics.
After each step have customer try to use data by googling something or looking up www.bbc.co.uk
From the Home Screen, swipe Up
Tap Settings
Tap Connections
Tap Mobile networks
Tap Network mode
Tap the required Network mode
If the customer is using the Dual SIM functionality on the handset and wants to use mobile data whilst on a call, they will need to be using the same line which is set up for Mobile Data – unless they have Mobile Data Switching activated. Once Mobile Data Switching is enabled, any time the customer tries to establish a Mobile Data connection whilst on a call, it will automatically switch to the other line if needed – this does not change the default data line.
Enable data roaming on
the device. Does this
resolve the problem?

## Slide 17
Is the device showing signal
strength? If no follow path
for No Signal.
The signal strength indicator is at the top of the screen.
If there's no signal displayed, the device will usually show a message such as No service or Emergency calls only.
If the customer has at least one bar or more displayed, it means that they're connected to the network and the device does have signal strength.
Some devices (particularly Android) may show an 'R' next to the signal strength indicator which would mean that the customer is roaming.
Switch device off/on and
Retest. Does this resolve
issue?
Perform a manual
Network search
Please note this activity cannot be completed during a call on the device.
De-activate any Wi-Fi connection and then within the network settings of the device the customer is able to switch the device from an automatic network selection to a manual.
By doing this the device will search and find any network operators that provide coverage in the area. This includes networks that the home network don't have roaming agreements with. To ensure the customer is exploring all options, get the customer to attempt to log on to ALL available networks that appear in the search and test before moving on to the next one.
IMPORTANT: If no networks show up in the list (only the one that the customer is already connected to) when carrying out the search, select No networks found. This is because you cannot log off the current network and log on to another.
Ensure automatic mode is re-enabled after testing in manual mode.
If the menu option is not available ensure that the SIM card is inserted correctly and securely locked in place. Referring to the device manual should show how to correctly insert the SIM.
If the above diagnostics don’t work who you gonna call….?
Zest4
Roaming Issues: Unable to Make Voice Calls (Android)
General Housekeeping:
Has the customer turned
on data roaming?
Has the customer tried
to turn aeroplane mode
on and off?
Is this affecting more
than just the customer i.e
anyone they are with? *
Is this happening in more
than one area?
Have you had issues
roaming before?
If none of the General
Housekeeping works
continue with
Diagnostics.
Manually logged on to a
Roaming network. Does
this resolve issue? ( test
call)
From the Home Screen, swipe Up
Tap Settings
Tap Connections
Tap Mobile networks
Tap Network operators
Tap the slider against Select automatically to turn off
Tap OK
Tap the Network to connect to

## Slide 18: Zest4 Contact Details
Tel: 0161 956 3300 Opt 1 Opt 1
Portal: Raise a Support Ticket via the Zest4 Customer Portal –https://zest4customers.com - ticket type: Network Issues
Email: service@zest4.com